## Slide 1: Electric and Hybrid Vehicles Technology
Dr. Sachin Argade

## Slide 2: Agenda
Syllabus
Class tests
Class Quizzes
Class Project
Mid Semester exam
End Semester exam

## Slide 3: EEM3202T: Electric and Hybrid Vehicle Technology
Teaching Scheme: TH: 03 Hours/Week | Credit TH: 03
Examination Scheme:
In Sem. Evaluation : 20 Marks
Mid Sem. Exam : 30 Marks
End Sem. Exam : 50 Marks
Total : 100 Marks

## Slide 4: Course Outcomes
At the end of the semester student should be able to
CEEM3202T_1: Infer basic architecture of EVs and HEVs, their subsystems
CEEM3202T_2: Interpret performance and selection of energy storage systems in EVs
CEEM3202T_3: Analyze battery management system
CEEM3202T_4: Interpret Power Electronics and Motor Controller subsystem in EVs

## Slide 5
Before MSE – 2 proctored class Tests (50 Marks each), (4 Marks)
  1st Test after finished 1.5 Units (Unit 1 full and Unit 2 half) Approx.=12 Jan
  2nd Test after finishing next 1.5 Units (Remaining Unit 2 and Unit 3 Complete) Approx.= 11 Feb
After MSE – 2 proctored class Tests (50 Marks each), (4 Marks)
  3rd Test after finished 1.5 Units (Unit 4 full and Unit 5 Half)
  4th Test after finishing next 1.5 Units (Remaining Unit 5 and Unit 6 Complete)
Class Project/ Case Study: Individual: Presentations and report (typed) will carry marks. (8Marks).
  It will be declared on 29th December 2025
Continuous in class quizzes, they will be surprise quizzes. (2 Marks)
Total for ISE = 20 Marks

## Slide 6
Make a 100 Pages note book for tests and quizzes. You should have it with you for each and every class. Quizzes can happen any time.
MSE- first 3 Units – 30 Marks
ESE- All 6 Units – 50 Marks

## Slide 7: Types of Vehicles
Conventional gasoline vehicle (gasoline fuel and ICE),
Hybrid vehicle (gasoline fuel, electrical drive, and large rechargeable battery),
Electric vehicle (high-capacity electrical battery and electrical drive/generator),
Hydrogen fuel cell vehicle (high-pressure hydrogen fuel tank, fuel cell, electrical drive),
Hydrogen internal combustion vehicle (high-pressure hydrogen fuel tank and ICE),
Ammonia-fueled vehicle (liquid ammonia fuel tank, ammonia thermo-catalytic decomposition and separation unit to generate pure hydrogen, hydrogen-fueled ICE).

## Slide 8: Why Electric?
The Origin Story: Early Electric Vehicles (1830s–1910).
The Great Pause: The Rise of the Internal Combustion Engine (ICE).
The Modern Rebirth: From Hybrid to High-Performance EVs.
The Imperative: Environmental & Climate Impact.
The Benefit: Social, Health, and Economic Importance.

## Slide 9: EV History, Part I: Faster Than the Ford
1830s: Early prototypes by pioneers like Anderson and Parker.
1900: Peak Popularity—Nearly 1/3 of vehicles in the U.S. were electric.
Key Advantages: Quiet, odourless, and easy to operate (no manual cranking).
Target Market: Highly popular with women and urban drivers.

## Slide 10: EV History, Part II: The End of the First Era
1908: Henry Ford's Model T introduces mass-production, making gasoline cars affordable.
1912: The invention of the Electric Starter eliminates the dangerous hand-crank for ICE cars.
Infrastructure: Cheap, abundant oil and better roads favored long-distance ICE travel.
Outcome: EVs were relegated to niche uses by the 1930s.

## Slide 11: The Modern Revival: The Road to High-Performance
1970s: Oil crises spur renewed interest in alternatives (briefly).
1997: Toyota Prius popularizes the Hybrid Electric Vehicle (HEV) concept.
1990s: Government mandates (e.g., California ZEV) prompt corporate development (GM EV1).
2008: Tesla utilizes Lithium-ion batteries to deliver high performance and long range, launching the modern EV era.

## Slide 13: Overview of Electric Vehicles
Nitrogen Oxides
Carbon Monoxide
Unburned Hydrocarbons
Other Pollutants
Global Warming

## Slide 16
Petroleum resources

## Slide 19: Societal Benefits: Quieter, Healthier Communities
Public Health: Reduced air pollution leads to fewer respiratory illnesses and early deaths in cities.
Noise Reduction: Significantly quieter motors reduce noise pollution, improving urban tranquility.
Energy Security: Reduces reliance on volatile global oil markets, stabilizing national energy supply.
V2G Potential: Vehicle-to-Grid technology allows EVs to support the grid during peak demand.

## Slide 20: Economic Impact: Lower Costs, New Opportunities
Fuel Cost Savings: Electricity is significantly cheaper per mile than gasoline in most regions.
Lower Maintenance: Fewer moving parts means reduced service needs (no oil changes, fewer brake pad replacements).
Job Creation: Growth in battery manufacturing, charging infrastructure installation, and software development.
Global Competitiveness: Positioning nations as leaders in future transportation technology.

## Slide 21: The Environmental Imperative: Cleaning the Air
Zero Tailpipe Emissions: Immediately removes harmful pollutants (NOₓ, PM) from dense urban areas.
Lower Lifetime Emissions: Even with manufacturing and grid energy, EVs generally result in lower lifetime CO₂ than ICEs.
Grid Decarbonization: EV benefits grow substantially as power generation shifts to renewables (Solar, Wind).
Energy Efficiency: Electric motors convert approx. 77\% of energy to motion, vs. 12–30% for ICEs.

## Slide 22: environmental impact analysis
All stages of the life cycle were considered, starting from
  The extraction of natural resources to produce materials and
  Ending with conversion of the energy stored onboard the vehicle into mechanical energy for vehicle displacement and
  Other purposes (heating, cooling, lighting, etc.).
In addition, vehicle production stages and end-of-life disposal are considered
As it contributes to environmental impact

## Slide 23: Economical Analysis
Vehicle price,
Fuel cost, and
Driving range.
Maintenance costs
Cost of Battery replacement in Evs and HEVs

## Slide 25: Environmental Analysis
Air pollution (AP)
  The main GHGs were CO2 , CH4 , N2O, and SF6 (sulfur hexafluoride), which have GHG impact weighting coefficients relative to CO2 of 1, 21, 310, and 24,900, respectively.
Greenhouse gas (GHG) emissions
  For AP, the airborne pollutants CO, NOX , SOX , and VOCs are assigned the following weighting coefficients: 0.017, 1, 1.3, and 0.64, respectively.

## Slide 26
The vehicle production stage contributes to the total life cycle environmental impact through the pollution associated with
The extraction and processing of material resources,
Manufacturing and
The vehicle disposal stage.
Additional sources of GHG and AP emissions were associated with the fuel production and utilization stages

## Slide 28: electricity production
Regarding electricity production for the electric cars
  when electricity is produced from renewable energy sources and nuclear energy;
  when 50% of the electricity is produced from renewable energy sources and 50% from natural gas at an efficiency of 40%;
  when electricity is produced from natural gas at an efficiency of 40%.

## Slide 30: Results of technical–economical–environmental Analysis:
This analysis showed that the hybrid and electric cars have advantages over the others
If electricity is generated from renewable energy sources, the electric car is advantageous to the hybrid vehicle
If the electricity is generated from fossil fuels, the electric car remains competitive only if the electricity is generated onboard.
If the electricity is generated with an efficiency of 50–60% by a gas turbine engine connected to a high-capacity battery and electric motor, the electric car is superior in many respects.
For electricity-generation scenarios 2 and 3, using ammonia as a means to store hydrogen onboard a vehicle is the best option among those analyzed

## Slide 31: Key Hurdles to Mass Adoption
Charging Infrastructure: Expanding accessible public fast-charging networks across all routes.
Battery Technology: Reducing costs, improving density, and accelerating charging speeds (e.g., solid-state).
Raw Materials: Ensuring ethical sourcing and implementing robust battery recycling programs.
Initial Cost: Making EVs affordable for the mass market without heavy subsidies.

## Slide 34
Vehicle Acceleration (According to newtons second law)
is the total tractive effort of the vehicle
Is the total resistance,
Mv is the total mass of the vehicle, and δ is the mass factor,

## Slide 35
Total Tractive Force
Rolling Resistance Force(Frr)
Aerodynamic drag force(Faero)
Hill climbing Force(Fhc)
Acceleration Force(Fxi)
    Linear Acceleration Force
    Angular acceleration force

## Slide 36: Total Power Required
Total Power P = Fte . V
Fte (Total Tractive Power) = Frr + Fad + Fhc + Fla + Fwa
Frr - Rolling Resistance Force
Fad – Aerodynamic Drag Force
Fhc - Hill Climbing Force
Fla - Linear Acceleration Force
Fwa - Angular Acceleration Force
Frr = µrr m.g
µrr - Rolling Resistance Constant
m - Mass of the Vehicle
g - Gravitational acceleration constant
Rolling Resistance Force

## Slide 39
Aerodynamic Drag Force
Fad = ½ρCdAv2 Newtons
ρ – Air Density kg/m3
A – Frontal Area m2
Cd – Drag Coefficient
v - Velocity of the Vehicle m/s
Reference values for drag coefficient (CD) and the frontal area (Af in m2) for some vehicle types

## Slide 41
Hill Climbing Force
Fhc = m.g.Sin θ
Linear Acceleration Force
(Fla) = m.a
Rise / Run
Fhc = m.g.Sin θ
Run
Rise
Length
θ
Θ varies from 0 – 10 degree hill

## Slide 42
Angular Acceleration
I= Moment of Inertia
G= Gear ratio
a = Acceleration
r = radius of tire
= Efficiency of Gear

## Slide 43
Parameters | Notations | Value | Units
Weight | m | 1,000.00 | Kg
Width | W | 1.00 | m
Height | H | 1.50 | m
Rolling Resistance | µrr | 0.02 | 
Air Density | ƥ | 1.25 | kg/m2
Drag Coefficient | Cd | 0.30 | 
gravitational Force | g | 9.80 | 
Speed in km |  | 40.00 | kpmh
Frontal Area | A | 1.50 | m2
Velocity | v | 11.11 | m/sec

## Slide 44
Total Power = Total Tractive Force x Velocity
Velocity = kmpm -> m/s
= 40 * 1000/3600
Tractive Force =
Rolling Resistance Force + Aerodynamic drag force
Total Power P = Fte . v
Fte (Total Tractive Power) = Frr + Fad
Tractive Force | Fte | 230.72 | Nm
Total Power for 40Km | P | 2,563.58 | Watts

## Slide 48: Motor Operating Region
Torque
Speed
Constant Torque Region
Constant Power Region
ωc
(Base Speed or critical speed)
P = T. ω
POwer

## Slide 49
The Maximum torque of an electric vehicle is a simple function of angular speed.
Mostly low speeds, the maximum torque is a constant
Until the motor speed reaches a critical value after which the torque falls.

## Slide 51: Observation
Huge Variation in Motive power
Vehicle is fully loaded to unloaded condition
Vehicle in hill climbing condition
Vehicle Speed
While Calculating Vehicle Power, all the extreme conditions to be taken in to consideration
Eg: Typical Extreme Conditions
Over load : 20% of Full load
Gradience : 20%

## Slide 52: Acceleration of Force
The Vehicle will not be at constant speed.
Dynamic equation for Acceleration force (dv/dt)
m.dv/dt = Ft - (Frr + Fad + Fhc )
The Tractive Force greater than all resistance forces results into acceleration, similarly deceleration

## Slide 53: How fast can vehicle reach the top speed?
Limiting Factors I
  Weight of vehicle
  Motor power of vehicle
Limiting Factors II
  The Drive wheels will spin on the ground if, tractive effort>adhesive capability between tire and ground
  Significant Slipping on the ground for wet, icy, snow covered or soft soil
  Irrespective of the maximum torque power train can apply on wheel

## Slide 54: How fast can vehicle reach the top speed?
Slip S (Tire) = (1 – V/rω) * 100% for running
Slip S (Tire) = (1 – rω/V) * 100% For Breaking
V – Translatory Speed of Tire center,
w – Angular speed of tire,
r – Rolling radius of the tire

## Slide 56
Total Power P = Fte . v
Fte Total Tractive Power = Frr + Fad + Fhc + Fla + Fwa
Frr = µrr m.g
Fad = ½ρCdAv2 Newtons
Fhc = m.g.Sin θ
(Fla) = m.a

## Slide 57: Conclusion: Driving the Future
EVs are a proven technology with deep historical roots.
The shift is crucial for climate mitigation and local air quality.
The transition offers tangible social and economic benefits (health, cost savings).
Continued innovation in batteries and infrastructure will define the next decade of mobility.