## Slide 1: Regenerative Braking
Dr. Sachin Argade

## Slide 2: Why Braking is an Energy Problem
A moving vehicle carries kinetic energy that was supplied by the battery or fuel during previous acceleration.
In a conventional brake system, almost all of that useful energy is discarded as heat at the disc and pad interface.
In urban driving, where start-stop events are frequent, recovering even a fraction of that energy produces a noticeable improvement in efficiency and range.

## Slide 3: Kinetic Energy of a Vehicle
The total translational kinetic energy stored in a vehicle is proportional to mass and to the square of speed.
This immediately tells us two engineering facts: heavy vehicles waste more energy during each stop, and high-speed stops contain disproportionately large amounts of recoverable energy.
That is why buses, trains and EVs in hilly regions benefit strongly from regenerative braking.

## Slide 4: Kinetic Energy Equation
The translational kinetic energy of a vehicle is given by the expression shown at right.
In regenerative braking, this equation provides the theoretical upper bound on recoverable energy from a stop.
The actual electrical energy returned to the battery is lower because the machine, inverter, cables and battery all introduce losses.
Engineering interpretation
Mass increases the energy linearly, but speed increases it quadratically.
Therefore highway braking events or heavy-vehicle stops contain especially large energy-recovery potential.

## Slide 5: Meaning of the Equation
If the speed doubles, the kinetic energy becomes four times larger because velocity appears as a square term.
This is important because braking system sizing, brake thermal loading, and energy recovery potential are all highly speed-sensitive.
A regenerative system designed for city traffic therefore sees very different duty cycles from one designed for highway operation.

## Slide 6: Conventional Friction Braking
In a friction brake, calipers squeeze pads against a rotating disc.
The friction force creates a torque opposite to wheel rotation, so vehicle speed falls.
The braking energy appears primarily as heat in the disc, pad, tire and surrounding air.
This method is reliable and necessary for final stop and emergency braking, but it is fundamentally dissipative rather than energy conserving

## Slide 7: Thermal Consequences of Friction Braking
During repeated braking events the rotor temperature rises, which can lead to brake fade, thermal stress, increased pad wear and reduced service life.
Regenerative braking reduces the burden on friction brakes, which means lower maintenance cost and more stable brake temperatures in normal driving.

## Slide 8: Basic Idea of Regenerative Braking
Regenerative braking replaces part of the dissipative braking torque with electromagnetic braking torque.
Instead of forcing pads to absorb all the vehicle energy
  the control system commands the traction motor so that it resists wheel motion and
  simultaneously sends electrical power back through the inverter toward the battery.

## Slide 9: Motor Action in Propulsion
In propulsion mode, the inverter sends controlled current to the stator windings.
Those currents produce a rotating magnetic field.
The rotor attempts to align with that field, so torque is produced and the shaft turns.
Electrical input power is therefore converted into mechanical output power.

## Slide 10: Generator Action in Braking
In braking mode, the wheel side drives the shaft.
Once the rotor is being forced mechanically, the moving magnetic field induces voltage in the machine windings.
If the electrical conditions are correct, current reverses direction and the electromagnetic torque opposes rotation.
Mechanical input power is then converted to electrical output power.

## Slide 11: How a Motor Becomes a Generator
A motor does not need a physical hardware change to become a generator.
The same electromagnetic machine can do both jobs.
The operating mode depends on the relative directions of speed, torque and current.
When shaft motion is imposed by the vehicle and the machine develops torque opposite to that motion,
  it is absorbing mechanical power.
  That absorbed mechanical power emerges electrically and is directed back to the energy storage system.

## Slide 12: Back EMF Equation
Back EMF is proportional to speed and magnetic flux and is expressed as Eb = kΦω. During regeneration this voltage becomes larger than the supply voltage.
The exact constant depends on machine design, but the qualitative message is universal: faster rotor speed means larger internally generated voltage.
During regenerative braking, this machine-generated voltage becomes the source that drives current back to the DC link and then to the battery.
Why it matters
Low speed means low back EMF and weak regeneration. As speed rises, the machine can generate a larger voltage, making reverse power flow possible and controllable.

## Slide 13: When Back EMF Exceeds Supply Voltage
Regeneration requires the machine-side generated voltage to exceed the effective battery-side or DC-link voltage after accounting for inverter control.
When the rotor speed is sufficiently high, the back EMF becomes large enough that current naturally wants to flow from the machine toward the DC bus.
The inverter then controls that current so that charging remains within safe limits.

## Slide 14: Why This Happens During Braking
During deceleration the wheels are still rotating because of the vehicle’s inertia.
Through the driveline, they force the motor shaft to keep turning.
If the controller commands a negative torque request, the machine current phase is adjusted so electromagnetic torque opposes the motion.
The shaft is therefore doing work on the motor, and the motor responds by generating electrical power.

## Slide 15: Current Reversal and Power Reversal
Electrical power can be viewed as voltage multiplied by current, while mechanical power is torque multiplied by angular speed.
In forward motoring, both speed and torque are positive and power goes from battery to wheels.
In forward regeneration, speed stays positive but torque becomes negative, which means mechanical power at the machine is negative
from the machine’s perspective: power is flowing from the wheels into the electrical system.

## Slide 16: Four-Quadrant Operation: Why It Matters
The easiset way to understand regenerative braking is through the four-quadrant torque-speed plane.
The horizontal axis is speed and the vertical axis is torque.
Each quadrant tells us whether the machine is motoring or generating and whether the vehicle is moving forward or backward.

## Slide 17: Torque-Speed Plot with Regenerative Region
Quadrant II is highlighted because it is the normal forward regenerative braking region.
Positive speed means the car is still moving forward.
Negative torque means the machine is applying torque opposite to rotation.
Together these signs indicate generating operation and explain why the vehicle slows while the battery receives charge.
Torque
Speed
Q2
Forward
regen
Q1
Forward
motoring
Q3
Reverse
motoring
Q4
Reverse
regen
Generating when speed and torque have opposite signs

## Slide 18: Reading the Torque-Speed Plot
The sign of torque tells you whether the machine is trying to assist the motion or oppose it.
The sign of speed tells you the rotation direction.
The sign of mechanical power is their product.
If torque and speed have the same sign, the machine is motoring.
If torque and speed have opposite signs, the machine is generating.

## Slide 19: Quadrant I: Forward Motoring
In Quadrant I, speed is positive and torque is also positive.
The vehicle is moving forward and the motor is driving it forward.
Mechanical output power is delivered to the wheels.
This is the region used during normal forward acceleration and cruising assistance.

## Slide 20: Quadrant II: Forward Regenerative Braking
In Quadrant II, speed remains positive but torque becomes negative.
The vehicle is still moving forward, yet the machine now resists the rotation.
This is the classic forward regenerative braking region.
The wheels provide mechanical input and the electrical system receives the recovered power.

## Slide 21: Quadrant III: Reverse Motoring
In Quadrant III, both speed and torque are negative.
The vehicle is moving backward and the motor is also driving in the backward direction.
From the power point of view this is still a motoring region because the battery is supplying the machine.

## Slide 22: Quadrant IV: Reverse Regenerative Braking
In Quadrant IV, speed is negative but torque becomes positive.
This means the vehicle is moving backward while the machine torque acts opposite to that motion.
Regeneration therefore also exists in reverse.
Although it is less discussed, the physics is exactly analogous to forward regeneration.

## Slide 23: Regenerative Braking Torque
The braking torque magnitude depends on flux, machine constant and current.
Higher regenerative current creates stronger negative torque, but the allowable value is limited by
  battery charging current,
  inverter thermal limits,
  tire adhesion
  and passenger comfort.
Therefore the strongest possible regeneration is not always the most desirable operating point.

## Slide 24: Battery SOC vs Regenerative Braking Limits
A battery with low state of charge can accept more charging current, so the available regenerative-power limit is high.
As the battery fills, charge acceptance falls.
When SOC is very high, the controller must reduce regenerative torque and hand more of the stopping task to the friction brakes.
Regen limit
SOC
high
low
However, batteries cannot accept arbitrary current under all conditions.
Their allowable charging power depends on chemistry, temperature, internal resistance and state of charge.

## Slide 25: Why Low Speed is a Problem
At very low speed, back EMF is small because it is proportional to angular velocity.
If the generated voltage is too low, the machine cannot push significant current into the DC bus.
Therefore regeneration fades out as the vehicle approaches standstill, and friction brakes must supply the final stopping torque.

## Slide 26: Blended Braking
Because regenerative braking is limited by speed, battery condition and control constraints, production EVs use blended braking.
The supervisory controller combines regenerative torque and friction torque so the driver feels a smooth, predictable deceleration even when the regenerative portion changes.

## Slide 27: How Regeneration Happens in a Series Hybrid
During deceleration, the traction motor connected to the wheels switches into generator mode.
Its generated electrical power can recharge the battery or support the DC bus.
The engine path is separate from the wheel path, so the machine on the axle remains the main regenerative device.
The control problem is therefore similar to that of a pure EV, except that the energy management system must also coordinate the engine-generator set.

## Slide 28: How Regeneration Happens in a Parallel Hybrid
During brmachine.aking in a parallel hybrid, the driveline continues to spin the electric
If the engine is decoupled or its torque is reduced appropriately, the motor acts as a generator and recovers wheel energy.
In some designs the amount of recoverable energy is lower than in a series hybrid because the packaging and mechanical coupling constraints are tighter.
Nevertheless the physical principle is the same: negative machine torque converts wheel work into electrical power.

## Slide 29: Regenerative Power Curve vs Vehicle Speed
Regenerative braking capability is usually weak at very low speed,
strongest in a mid-speed window,
and then capped at higher speed by current, thermal or battery-charge limits.
The exact shape differs across vehicles, but the trend shown here is common across production EVs and hybrids.
Power
Speed
low-speed
fade-out
peak
limited

## Slide 30: Numerical Example 1
A 1600 kg battery electric car is traveling at 72 km/h on level road.
Estimate the translational kinetic energy available just before braking,
and
then compute the recovered energy if the regenerative system captures 65% of that value.
Solution :
First convert 72 km/h to 20 m/s.
Then kinetic energy is one-half times mass times velocity squared: 0.5 × 1600 × 20² = 320000 J.
If recovery efficiency is 65%, the stored electrical energy is 0.65 × 320000 = 208000 J.
This example shows that even a single moderate stop contains a meaningful amount of recoverable energy.

## Slide 31: Numerical Example 2
A bus of mass 9000 kg slows from 50 km/h to 10 km/h.
Compute the change in kinetic energy over that speed interval,
then
estimate recovered energy if only 55% of the lost kinetic energy can be captured because of converter and battery limits.
Solution :
Convert the speeds: 50 km/h = 13.89 m/s and 10 km/h = 2.78 m/s.
Initial kinetic energy is about 0.5 × 9000 × 13.89² ≈ 868000 J.
Final kinetic energy is about 0.5 × 9000 × 2.78² ≈ 34800 J.
The decrease is about 833200 J.
At 55% capture, recovered energy is approximately 458000 J.

## Slide 32: Application: Electric Trains and Electric Buses
Electric trains are ideal candidates for regeneration because they are heavy, operate on fixed routes and experience repeated acceleration and braking.
In electrified rail networks the recovered energy can sometimes be returned directly to the grid or used by nearby trains, making system-level savings substantial.
City buses brake many times per route, so regenerative braking provides large cumulative savings.
Because buses are massive, each stop contains significant kinetic energy.
Regeneration also reduces brake maintenance, which is economically valuable in fleet operation.

## Slide 33: Design trade-offs and practical approach
While designing we must balance energy recovery against safety, comfort and battery health.
Excessive regenerative torque can disturb vehicle stability on slippery roads. Excessive charging current can damage the battery.
Very aggressive deceleration can also feel unnatural to passengers.
Good calibration therefore matters as much as the physics.

## Slide 34
Summary
Regenerative braking is not merely a clever add-on.
It is a central efficiency technology for EVs and hybrids.
The key ideas are straightforward once organized:
wheel motion forces the motor to generate, back EMF and current direction determine when power can flow to the battery.
The torque-speed plane explains the sign changes, and real vehicles use control logic plus friction blending to make the system safe and effective.