## Slide 1: Parallel_Hybrid
Dr. Sachin Argade

## Slide 2: Introduction to Parallel Hybrid Drive
Parallel hybrid vehicles use both an internal combustion engine and an electric motor to drive the wheels.
Both sources can operate individually or simultaneously depending on power demand.
This architecture improves efficiency and performance.

## Slide 3: Parallel Hybrid Mode

## Slide 4: Definition of Parallel Hybrid
In a parallel hybrid system the engine and motor are mechanically connected to the drivetrain.
Both can supply torque to the wheels.
This differs from series hybrids where only the motor drives the wheels.

## Slide 5: Basic Components
Engine
Electric Motor
Battery Pack
Power Electronics
Transmission and Differential

## Slide 6: Power Flow in Parallel Hybrid
Mechanical power from engine flows directly to wheels.
Motor can add torque or absorb energy during braking.

## Slide 7: Torque Equation
Total torque at wheels is sum of engine torque and motor torque.
T_total = T_engine + T_motor.
Power Equation
Total power delivered to wheels:
P_total = P_engine + P_motor.

## Slide 8: Energy Flow
Fuel energy is converted to mechanical energy by engine.
Battery energy is converted to mechanical energy by motor.
Acceleration Mode
During acceleration both engine and motor provide torque.
This improves vehicle performance.

## Slide 9: Cruise Mode
At steady speed engine alone may provide power.
Motor may remain idle or charge battery.
Electric Mode
At low speed motor alone may drive the vehicle.
This reduces fuel consumption.

## Slide 10: Regenerative Braking
Motor acts as generator during braking.
Kinetic energy is converted into electrical energy.
Vehicle kinetic energy : E = 1/2 m v².
Energy Equation for Regeneration

## Slide 11: Battery Role
Battery stores recovered energy from regenerative braking.
It supplies energy to motor during electric drive mode.
SOC Concept
State of Charge represents remaining battery capacity.
Control system maintains SOC within safe limits.

## Slide 12: Motor Characteristics
Motor provides high torque at low speed.
This is useful during vehicle start.
Engine Characteristics
Engines are efficient at moderate to high loads.
Parallel hybrid allows engine to operate efficiently.

## Slide 13: Engine and Motor Cooperation
Motor assists engine when high power demand occurs.
Engine supplies base power.
Driver Demand Analysis
Acceleration request determines torque requirement.
Controller decides motor assist level.

## Slide 14: Motor Torque-Speed Map
Electric motors deliver high torque at low speeds.
Torque decreases as speed increases due to voltage limits.
This characteristic allows motors to assist during vehicle start and acceleration.
Torque-speed map helps in selecting motor size for hybrid systems.

## Slide 15: Engine Torque-Speed Characteristics
Internal combustion engines produce maximum torque in mid RPM range.
Torque decreases at very high RPM due to breathing limitations.
Hybrid control system combines engine torque curve with motor torque curve.
This provides a wider effective torque-speed operating region.

## Slide 16: Power Flow – Electric Mode
Battery
Inverter
Motor
Transmission
Wheels

## Slide 17: Power Flow – Engine Mode
Fuel Tank
Engine
Transmission
Wheels

## Slide 18: Power Flow – Hybrid Assist Mode
Fuel
Engine
Transmission
Wheels
Battery
Inverter
Motor

## Slide 19: Energy Flow During Regenerative Braking
Wheels
Motor (Generator)
Inverter
Battery

## Slide 20: How Parallel Hybrid Decides Engine vs Motor Operation
Hybrid Control Unit (HCU) monitors driver power demand, vehicle speed, battery SOC, and engine efficiency region.
If power demand is small and battery SOC is sufficient, motor-only operation is selected.
If vehicle speed is high or battery SOC is low, engine operation is selected.
For high torque demand (acceleration), both motor and engine operate together.

## Slide 21: Typical Mode Selection Logic
Low speed + light load → Motor drive (electric mode).
Medium speed + moderate load → Engine dominant mode.
High acceleration demand → Hybrid assist mode (engine + motor).
Braking → Regenerative braking mode where motor acts as generator.

## Slide 22: Parallel Hybrid Mode Decision Flow
Driver Power Demand
Check Battery SOC
Low Power?
Motor Mode
High Power?
Hybrid Assist
Cruise
Engine Mode

## Slide 23: Torque Combination in Parallel Hybrid
In a parallel hybrid both the engine and motor deliver torque to the same drivetrain.
The gearbox combines torque from both sources before it reaches the wheels.
Total torque delivered to wheels is: T_total = T_engine + T_motor.
This allows the vehicle to achieve higher acceleration compared to a conventional engine vehicle.

## Slide 24: Complete Parallel Hybrid Drivetrain (Torque Flow)
Fuel Tank → Internal Combustion Engine
Produces Engine Torque (T_engine)
Electric Motor
Produces Motor Torque (T_motor)
Transmission / Gearbox
Combines Torque
Differential
Distributes Torque to Wheels
Drive Wheels
Receive Total Torque
T_total = T_engine + T_motor

## Slide 25: Combined Power-Speed Operating Map (Engine + Motor)
Electric motors provide high torque at low speed and gradually reduce torque at higher speed.
Internal combustion engines produce peak torque at medium RPM ranges.
When both systems are combined, the hybrid drivetrain provides a wide torque-speed operating region.
Motor supports the engine at low speeds while the engine dominates at higher speeds.

## Slide 26: Power-Speed Operating Regions
Low Speed Region
Motor Dominant Operation
High Starting Torque
Medium Speed Region
Engine + Motor Hybrid Assist
High Speed Region
Engine Dominant Operation
Motor Minimal Assist

## Slide 27: Hybrid Controller Mode Switching Logic
The Hybrid Control Unit (HCU) decides operating mode based on vehicle conditions.
Inputs include vehicle speed, driver power demand, battery state of charge (SOC), and engine efficiency region.
Controller continuously evaluates these parameters and switches operating modes.
Goal: maximize efficiency while maintaining performance.

## Slide 28: Real Hybrid Mode Switching Logic
Driver Power Demand Detected
Check Battery State of Charge (SOC)
Low Power Demand → Electric Motor Mode
High Power Demand → Hybrid Assist Mode (Engine + Motor)
Steady Highway Speed → Engine Dominant Mode

## Slide 29: Gears in Parallel Hybrid Drivetrain
Gears are used in parallel hybrids to combine torque from both the engine and electric motor.
The gearbox allows both power sources to transmit torque to the wheels through a common drivetrain.
This mechanical combination enables T_total = T_engine + T_motor.
Gears also allow proper speed matching between engine RPM, motor speed, and wheel speed.

## Slide 30: Typical Gear Arrangement in Parallel Hybrid
Internal Combustion Engine
Produces Engine Torque
Electric Motor
Produces Motor Torque
Clutch / Coupling Gear
Allows Torque Combination
Transmission Gearbox
Speed & Torque Adjustment
Differential
Transfers Torque to Wheels

## Slide 31: Types of Gear Systems Used in Parallel Hybrids
Parallel hybrid systems commonly use conventional automotive gearboxes.
Manual transmission, automated manual transmission, and dual clutch transmission can be used.
Planetary gear systems are sometimes used in more advanced hybrids.
Gear systems must withstand combined torque from engine and electric motor.

## Slide 32: Torque Flow Through Hybrid Gear System
Engine torque enters the transmission through the crankshaft.
Motor torque is injected through the motor shaft or integrated starter generator.
The gearbox combines these torques before transmitting power to the differential.
The differential distributes torque between left and right drive wheels.

## Slide 33: Gear Design Considerations in Parallel Hybrids
Gears must handle higher combined torque loads compared to conventional vehicles.
Proper gear ratios are required to match engine and motor operating speeds.
Transmission efficiency directly affects hybrid system efficiency.
Robust clutch systems are required to smoothly engage engine and motor torque.

## Slide 34: Planetary Gear Set in Hybrid Drivetrains
A planetary gear set is a compact gear mechanism used to combine or split power between multiple sources.
It consists of three main elements: Sun gear, Planet gears with carrier, and Ring gear.
In hybrid vehicles these gears allow engine torque and motor torque to be transmitted through the same drivetrain.
They are widely used in advanced hybrid systems because they allow flexible power flow.

## Slide 35: Planetary Gear Elements Used in Hybrid Systems
Sun Gear
Connected to Motor or Generator
Planet Gears + Carrier
Transmit and Combine Torque
Ring Gear
Connected to Engine or Transmission
Output Shaft
Power Delivered to Wheels

## Slide 36: Role of Planetary Gears in Hybrid Power Transmission
Planetary gears allow multiple power sources to be connected to the drivetrain simultaneously.
In many hybrids the engine connects to the ring gear while the motor connects to the sun gear.
The carrier transmits combined torque to the wheels.
This arrangement allows smooth blending of engine power and motor power without conventional gear shifting.

## Slide 37: Torque Split
Vehicle requires wheel torque of 350 Nm.
If engine provides 220 Nm and motor provides 130 Nm verify torque equation.
T_total = T_engine + T_motor = 350 Nm.
This demonstrates torque sharing in parallel hybrid systems.

## Slide 38: Power Split
Required wheel power = 90 kW.
Engine supplies 60 kW and motor supplies 30 kW.
Verify: P_total = P_engine + P_motor = 90 kW.
This demonstrates power balance in hybrid operation.

## Slide 39: Regenerative Energy
Vehicle mass = 1600 kg and speed = 22 m/s.
Kinetic energy = ½ m v² = 0.5 × 1600 × 484 = 387 kJ.
If regeneration efficiency = 60%, recovered energy = 232 kJ.

## Slide 40: BSFC Contour Map Explanation
Brake Specific Fuel Consumption (BSFC) maps show engine efficiency across speed and load.
Contours represent constant fuel consumption values in g/kWh.
Lowest BSFC region indicates most efficient engine operation.
Hybrid controllers attempt to operate engine near this region.

## Slide 41
Hybrid vehicles maintain engine operation near minimum BSFC region.
This reduces fuel consumption and emissions.
Electric motor handles transient load changes so engine remains efficient.
Optimal Engine Operating Region

## Slide 42: Driving Performance
City
Frequent acceleration allows motor assist.
Regenerative braking recovers energy.
Highway
Engine provides most of the power.
Direct mechanical path improves efficiency.
Why Parallel Hybrid is Good for Highway?
Minimal energy conversion losses.
Engine directly drives wheels.
Comparison with Series Hybrid
Series hybrid requires multiple energy conversions.
Parallel hybrid avoids electrical conversion losses.
Series hybrid experiences generator and inverter losses.
Parallel hybrid avoids these losses.

## Slide 43: Applications of Parallel Hybrid
Passenger vehicles
Highway vehicles
Honda Insight

## Slide 44: Series Hybrid Power Equation
In a series hybrid the engine does not drive the wheels mechanically.
Fuel power is converted to electrical power through generator before reaching wheels.
Power equation: P_wheel = η_m × η_g × η_e × P_fuel.
This means energy passes through multiple conversion stages.

## Slide 45: Parallel Hybrid Power Equation
In a parallel hybrid both engine and motor supply power directly to the drivetrain.
Power equation: P_total = P_engine + P_motor.
Torque equation: T_total = T_engine + T_motor.
This reduces electrical conversion losses compared with series architecture.

## Slide 46: Series Hybrid Energy Flow
Fuel
Engine
Generator
Motor
Wheels

## Slide 47: Parallel Hybrid Energy Flow
Fuel
Engine
Transmission
Wheels
Motor Assist

## Slide 48: Applications of Series Hybrid
Series hybrids are ideal for stop‑and‑go city driving.
Examples include buses, range‑extended electric vehicles, and urban delivery vehicles.
Reason: frequent braking allows regenerative energy recovery.
Electric motor handles propulsion smoothly at low speeds.

## Slide 49: Applications of Parallel Hybrid
Parallel hybrids are widely used in passenger cars and highway vehicles.
Examples include mild hybrids and full hybrids with direct drivetrain connection.
Reason: mechanical power path from engine to wheels provides higher highway efficiency.
Motor assists during acceleration and regenerative braking.

## Slide 50: Series vs Parallel Hybrid – Key Differences
Series hybrid: engine never drives wheels directly; all propulsion through motor.
Parallel hybrid: engine and motor both connected to drivetrain.
Series hybrid better for city cycles with frequent braking.
Parallel hybrid better for highway driving because mechanical power path reduces losses.

## Slide 51: Summary
Better highway efficiency
Improved acceleration
Reduced fuel consumption
Parallel hybrid combines engine and motor power.
Efficient for highway driving and moderate city driving.
Control strategies determine optimal operation.
Improved batteries and power electronics will enhance hybrid performance.
More complex mechanical system.
Control strategy complexity.